## Slide 1: Privacy Shield

## Slide 2: Team members
Gabriele Turchetti
Donaldo Buzi
Haron Obaid

## Slide 3: Idea
The project consists of a device that can be attached to doors or windows to mask the noise coming from a room.
The main goal is to mask a type of noise inside the room to prevent people outside from overhearing them.
This goal is accomplished by one or more devices that capture sound detect if there is a conversation or other type of noise, and mask it with the most appropriate sound emitted by a transducer attached to the door or window.

## Slide 4: Edge
In a multi-device network, a Leader is elected based on which node detects the highest noise intensity.
The Leader identifies the sound type, if it matches a specific target profile, it coordinates the Followers to emit a synchronized anti-noise signal to mask the disturbance.
Information about all devices is sent to the cloud to generate statistics and monitor the state of the network, such as battery levels, device reachability, and more.

## Slide 5: IoT
Configuration will be performed via a web application that a user can access when within the network's range.
The network status can be viewed either via the internal network or via the cloud if the user is remote.
The settings include which devices should be turned on or off, the intensity of the masking noise, the preferred noise type to emit, and so forth.

## Slide 6: Implementation plan
Audio Algorithm Update: Replaced the white noise concept with the Adaptive Masking Algorithm utilizing Pink or Brown noise for better acoustic masking.
Feedback Loop Fix: Added the requirement for an Acoustic Echo Cancellation (AEC) DSP pipeline to prevent infinite positive feedback between the microphone and the transducer.
Network Stability: Introduced hysteresis and threshold logic to the Dynamic Master-Slave election algorithm to prevent network thrashing when ambient noise fluctuates.
Cloud Privacy Clarification: Explicitly stated in Sprint 2 that cloud telemetry only sends timestamps and activation states.
Machine Learning Addition: Added a Sprint 3 requirement to implement an algorithm for recognizing and targeting power tool noise signatures.

## Slide 7: Hardware list
I2S Microphone
Dayton Audio DAEX25
MAX98357A Amplifier
22 AWG Speaker Wire
ESP32-S3 Microcontroller
Breadboard
Connectors
Battery

## Slide 8: Thank you for your attention